## Slide 1
Trapping and Tracing
in z/XDC (by David Cole)
Notes: Ok, I’m going to tell you everything you wanted to know about trapping and tracing.
I’m going to start off reading several slides,
<click1> But don’t worry. Soon enough there will be pictures.

## Slide 2: Tracing and Trapping
General Definitions
Trapping is setting a breakpoint at a point of interest and then capturing control when execution reaches that point.
Tracing is allowing the current one or more machine instructions to execute and recapturing execution upon a certain circumstance.
Hooking is setting a special kind of breakpoint, called a hook, that both captures execution and establishes z/XDC as the newest recovery routine (ESTAEX) for that point in your code. In other words, it sets up that code for debugging using z/XDC.
General Definitions
Trapping is setting a breakpoint at a point of interest and then capturing control when execution reaches that point.
Tracing is allowing the current one or more machine instructions to execute and recapturing execution upon a certain circumstance.
Hooking is setting a special kind of breakpoint, called a hook, that both captures execution and establishes z/XDC as the newest recovery routine (ESTAEX) for that point in your code. In other words, it sets up that code for debugging using z/XDC.
Notes: <implied click> [Hide the text]
Read the slide for 4 clicks.

## Slide 3: Tracing and Trapping
General Definitions (cont.)
Traps and Trace points are implemented by setting X’00’ opcodes at the points where execution is to be recaptured. These opcodes cause your program to program check. z/XDC intercepts those program checks and interprets them as breakpoints.
Hooks are implemented by setting an SVC instruction at the point where execution is to be intercepted and a z/XDC debugging session is to be established.
  Generally you would use a Hook at a place in your code where a debugging session needs to be established, and then you would use Traps and Traces from then on for stepping through your code.
  A z/XDC sessions needs to be established in any piece of code that you want to debug and for which z/XDC is not yet the newest recovery routine (ESTAE[X] or ESTAI).
General Definitions (cont.)
Traps and Trace points are implemented by setting X’00’ opcodes at the points where execution is to be recaptured. These opcodes cause your program to program check. z/XDC intercepts those program checks and interprets them as breakpoints.
Hooks are implemented by setting an SVC instruction at the point where execution is to be intercepted and a z/XDC debugging session is to be established.
  Generally you would use a Hook at a place in your code where a debugging session needs to be established, and then you would use Traps and Traces from then on for stepping through your code.
  A z/XDC sessions needs to be established in any piece of code that you want to debug and for which z/XDC is not yet the newest recovery routine (ESTAE[X] or ESTAI).
Notes: <implied click> [Hide the text]
Read the slide for 4 clicks.

## Slide 4: Tracing and Trapping
General Statements
Traps and Hooks can be Live or Deferred:
  A Live trap or hook is one that is set into code in storage.
  A Deferred trap or hook is one that will be set only when the targeted load module is brought into storage (via LOAD, LINK, ATTACH[X] or XCTL).
Traps can be Permanent or Transient:
  Permanent: Remains until explicitly removed by an OFF command.
  Transient: Is automatically removed when it is reached by execution.
Traps and Traces can be Conditional: They will not “be accepted” until a specified condition resolves TRUE:
  Counting Conditions: The trap must be reach n number of times.
  Boolean Expressions: Tests values in registers and/or storage.
Traps and Traces may have Custom Command Strings to be executed when they are reached and accepted.
Traps and traces may be collected into Families for collective removal.
General Statements
Traps and Hooks can be Live or Deferred:
  A Live trap or hook is one that is set into code in storage.
  A Deferred trap or hook is one that will be set only when the targeted load module is brought into storage (via LOAD, LINK, ATTACH[X] or XCTL).
Traps can be Permanent or Transient:
  Permanent: Remains until explicitly removed by an OFF command.
  Transient: Is automatically removed when it is reached by execution.
Traps and Traces can be Conditional: They will not “be accepted” until a specified condition resolves TRUE:
  Counting Conditions: The trap must be reach n number of times.
  Boolean Expressions: Tests values in registers and/or storage.
Traps and Traces may have Custom Command Strings to be executed when they are reached and accepted.
Traps and traces may be collected into Families for collective removal.
Notes: Here are some more general statements.
I’ll get into the details as we go through the lesson.
Read the slide for 11 clicks.

## Slide 5: Traps
AT command: Creates Permanent traps. Can be removed only by OFF commands.
TRAP command: Creates Transient traps. Will be removed when they are reached by execution.
ATX command: Creates Permanent traps that are particularly hard to remove. These traps must be specifically referenced by an OFF command. They will not be removed by categorical references.
AT command: Creates Permanent traps. Can be removed only by OFF commands.
TRAP command: Creates Transient traps. Will be removed when they are reached by execution.
ATX command: Creates Permanent traps that are particularly hard to remove. These traps must be specifically referenced by an OFF command. They will not be removed by categorical references.
Notes: So we have Traps, Traces and Hooks. Here, I’m going to focus on Traps.
There are three commands that create traps...
Read the slide for 3 clicks.

## Slide 6
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------------------------------
XDC ===> WHERE
_ 00000000_0000DF80 8f (A.S.XDCDEMO) --- XDCSYMED+0, @R15+0, PRIVATE+BF80
_ +0 >@CDP EQU * @R15
_ +0 47F0 F06E >XDCSYMED B X'06E'(,R15) (XDCSYMED+6E)
_ +4 69C5 D5E3 CD FR12,X'5E3'(R5,R13)
_ +8 D9E8 40F1 F061 MVCK X'0F1'(R14,R4),X'061'(R15),R8
_ +E F1F2 61F1 F140 MVO X'1F1'(16,R6),X'140'(3,R15)
_ +14 F0F7 4BF5 F840 SRP X'BF5'(16,R4),X'840'(R15),7
_ +1A 6040 A961 STD FR4,X'961'(,R10)
_ +1E E7C4C36B 40C3D6D7 E8D9C9C7 C8E3404D C35D40C3 D6D3C5E2 D6C6E340 D7C1D9E3 *XDC, COPYRIGHT (C) COLESOFT PART*
_ +3E D5C5D9E2 6B40C9D5 C34B4060 40F2F0F0 F360F2F0 F1F14B40 C1D3D340 D9C9C7C8 *NERS, INC. - 2003-2011. ALL RIGH*
_ +5E E3E240D9 C5E2C5D9 E5C5C47A 40404000 90ECD00C 181D41D0 F08850D0 10085010 *TS RESERVED: ...}... }0h&}..&.*
_ +7E D0045810 101847F0 D0480000 00000000 00000000 00000000 00000000 00000000 *}......0}.......................*
_ +9E 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 *................................*
_ +BE 00000000 00000000 00000000 00000000 000047F0 D06C0000 E06856E0 D0680B0E *...................0}%..\..\}...*
_ +DE 41E0E000 58F0F00E 0B0F8500 E05E8000 00008000 00004DE0 D0505810 021C5810 * \\..00...e.\;........(\}&......*
_ +FE 100C4100 00181A10 BF011000 4780D0AA D507D910 10044770 D07C4D10 D09C8F00 *.. ...........}.N.R.....}@(.}...*
_ +11E 00000000 E8F01801 1B110A13 4110DD22 45E0D7E6 07004D10 D0B88000 00000000 *....Y0...... ....\PW..(.}.......*
_ +13E E8301801 1B110A13 07004D10 D0CC8F00 00000000 E8901801 1B1118F0 58F0F004 *Y.........(.}.......Y......0.00.*
_ +15E D202F025 D04D41F0 D80C50F0 D0649680 D0640A13 070047F0 D0FC00FF FFF80000 *K.0.}( 0Q.&0}.o.}......0}....8..*
_ +17E 10000000 007A9801 D0F058F0 D0F80A78 9001DA5C 1E015000 DA649640 DA5A4110 *.....:q.}0.0}8.....*..&...o .! .*
_ +19E D8281FFF BFF71031 4100D5A4 A700FF00 A7740004 BE071021 91841020 A7E40006 *Q....7.. .Nux...x.......jd..xU..*
_ +1BE 58E01000 5000E028 0DEF4100 00015E00 DA405000 DA401821 D5032000 DAC44780 *.\..&.\... ...;.. &.. ..N....D..*
_ +1DE D1764110 D8881802 1FFFBFF7 10310DEF 41000001 5E00DA44 5000DA44 47F0D114 *J. .Qh.....7.... ...;...&....0J.*
_ +1FE 9801DA60 5000DA68 5000DA6C 5010DA70 94BFDA5A 1F44F840 DB96DC0C D207DB0C *q..-&...&..%&...m..!..8 .o..K...*
_ +21E 2048D205 DB86DB92 95F1DB13 4770D244 92FFDB0B 41000001 4110DB13 05E00610 *..K..f.kn1....K.k... ... ....\..*
_ +23E 060095F0 1000078E D205DB86 DB8C1000 89000004 43F0DB87 54F0DBC0 160F4200 *..n0....K..f....i....0.g.0.{....*
_ +25E DB874110 100143F0 DB8888F0 000447F0 D1EA1F10 44F0D1E8 5410DBC4 89F0000C *.g ....0.hh0...0J....0JY...Di0..*
_ +27E 161FBE13 DB8847F0 D2444110 D8281FFF BFF71031 4100D5A4 A700FF00 A7740004 *.....h.0K. .Q....7.. .Nux...x...*
_ +29E BE071021 91841020 A7E40006 58E01000 5000E028 0DEF4100 00015A00 DA405000 *....jd..xU...\..&.\... ...!.. &.*
_ +2BE DA401821 D5032000 DAC44770 D41441F4 DB3BD237 F0002010 41000038 BD03200A *. ..N....D..M. 4..K.0... ...]...*
Raw Unmapped Display
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------------------------------
XDC ===> MAP +0;SET QUALIFIER +0;WHERE;DOWN M
_ 00000000_0000DF80 8f (A.S.XDCDEMO) --- XDCSYMED.DBCSYMED+0, @R15+0, XDCSYMED+0, PRIVATE+BF80
_ .+0 >DBCSYMED CSECT , 07200000
_ .+0 > @DBCCB , 07500000
_ .+0 >DBCSYMED LOCTR , 09/02 Z12 01-00000
_ .+0 > TITLE 'OBJECT DECK SYMBOL TABLE EDITOR' 09/93 X22 07600000
_ .+0 > @TITLE 'OBJECT DECK SYMBOL TABLE EDITOR' 09/98 X34 01-00000
_ .+0 >************************************************************* 07700000
_ .+0 >* STANDARD NON-REENTRANT ENTRY LINKAGE * 07800000
_ .+0 >************************************************************* 07900000
_ .+0 >ENTRY #ENTER '&XNAME, &COPYRIT: ', 10/90 X21*08100000
_ .+0 > SAVTYPE=(LOCAL,SYMEDRSA), RSA TYPE AND NAME 05/97 X33*08200000
_ .+0 > ESDTYPE=ENTRY 10/90 X21 08400000
_ .+0 > ENTRY ENTRY MAKE NAME EXTERNALLY AVAILABLE 01-#ENTE
_ .+0 47F0 F06E >ENTRY B E0131ZID-ENTRY(,R15) X01-#ENTE
_ .+0 > SKIP AROUND THE MODULE ID
_ .+0 >ENTRY EQU * DBCSYMED @CDP @R15
_ .+0 47F0 F06E >XDCSYMED B X'06E'(,R15) (.E0131ZID)
_ .+4 69 + DC AL1(E0131ZID-E0131MID) X01-#ENTE
_ .+4 + LENGTH OF TEXT
_ .+5 C5D5E3D9 E840 +E0131MID DC C'ENTRY ' ENTRY NAME 01-#ENTE
_ .+B F1F061F1 F261F1F1 + DC C'12/07/11 ' ASSEMBLY DATE 01-#ENTE
_ .+13 40 o 64 * *
_ .+14 F0F74BF5 F8406040 + DC C'15.21 - ' ASSEMBLY TIME 01-#ENTE
_ .+1C A961E7C4 C36B40C3 + DC C'z/XDC, COPYRIGHT (C) COLESOFT PARTNERS, INC. - 2003-20X01-#ENTE
_ .+1C + 11. ALL RIGHTS RESERVED: '
_ .+24o D6D7E8D9 C9C7C8E3 404DC35D 40C3D6D3 C5E2D6C6 E340D7C1 D9E3D5C5 D9E26B40 *OPYRIGHT (C) COLESOFT PARTNERS, *
_ .+44o C9D5C34B 406040F2 F0F0F360 F2F0F1F1 4B40C1D3 D340D9C9 C7C8E3E2 40D9C5E2 *INC. - 2003-2011. ALL RIGHTS RES*
_ .+64o C5D9E5C5 C47A4040 40 *ERVED: *
_ .+6Do 00 0 *.*
_ .+6E 90EC D00C +E0131ZID STM R14,R12,12(R13) SAVE CALLER'S REGISTERS 01-#ENTE
ADATA Mapped Display
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------------------------------
XDC ===> SET FORMAT OBJECT;WHERE
_ 00000000_0000DF80 8f (A.S.XDCDEMO) --- XDCSYMED.DBCSYMED+0, @R15+0, XDCSYMED+0, PRIVATE+BF80
_ .+0 >ENTRY EQU * DBCSYMED @CDP @R15
_ .+0 47F0 F06E >XDCSYMED B X'06E'(,R15) (.E0131ZID)
_ .+4 69 105 *.*
_ .+5 E0131MID C5D5E3D9 E840 *ENTRY *
_ .+B F1F061F1 F261F1F1 40 *10/12/11 *
_ .+14 F0F74BF5 F8406040 *07.58 - *
_ .+1C A961E7C4 C36B40C3 D6D7E8D9 C9C7C8E3 404DC35D 40C3D6D3 C5E2D6C6 E340D7C1 *z/XDC, COPYRIGHT (C) COLESOFT PA*
_ .+3C D9E3D5C5 D9E26B40 C9D5C34B 406040F2 F0F0F360 F2F0F1F1 4B40C1D3 D340D9C9 *RTNERS, INC. - 2003-2011. ALL RI*
_ .+5C C7C8E3E2 40D9C5E2 C5D9E5C5 C47A4040 40 *GHTS RESERVED: *
_ .+6D 00 0 *.*
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
_ .+72 181D LR R1,R13
_ .+74 41D0 F088 LA R13,X'088'(,R15)
_ .+78 50D0 1008 ST R13,X'008'(,R1)
_ .+7C 5010 D004 ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
_ .+88 SYMEDRSA 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 *................................*
_ .+A8 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 *................................*
_ .+C8 00000000 00000000 *........*
_ .+D0 47F0 D06C E0131END B X'06C'(,R13)
_ .+D4 @EXLST 0000E068 .EXLST *..\.*
_ .+D8 OLDIO EQU *
_ .+D8 56E0 D068 XAMODE31 O R14,X'068'(,R13)
_ .+DC 0B0E BSM 0,R14
_ .+DE 41E0 E000 ODCBX LA R14,X'000'(,R14)
_ .+E2 58F0 F00E L R15,X'00E'(,R15)
_ .+E6 0B0F BSM 0,R15
_ .+E8 EXLST 8500E05E FLMS7C.X#1+BB05E *e.\;*
Mapped Object Code Display
Notes: <implied click1> Here is a program I’m going to use for demo purposes.
This display is raw, unmapped, ugly and incorrect.
<click2> Data is being misinterpreted as instructions.
<click3> And instructions are being misinterpreted as data.
<click4> But after I load an ADATA map, the disassembly is much more accurate.
Maps are pretty important, don’t you think?
But for my purposes, I think this is a bit over cluttered.
<click5> So I prefer to display the program as mapped object code, like so.
But I digress.

## Slide 7
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------------------------------
XDC ===> SET FORMAT OBJECT;WHERE
_ 00000000_0000DF80 8f (A.S.XDCDEMO) --- XDCSYMED.DBCSYMED+0, @R15+0, XDCSYMED+0, PRIVATE+BF80
_ .+0 >ENTRY EQU * DBCSYMED @CDP @R15
_ .+0 47F0 F06E >XDCSYMED B X'06E'(,R15) (.E0131ZID)
_ .+4 69 105 *.*
_ .+5 E0131MID C5D5E3D9 E840 *ENTRY *
_ .+B F1F061F1 F261F1F1 40 *10/12/11 *
_ .+14 F0F74BF5 F8406040 *07.58 - *
_ .+1C A961E7C4 C36B40C3 D6D7E8D9 C9C7C8E3 404DC35D 40C3D6D3 C5E2D6C6 E340D7C1 *z/XDC, COPYRIGHT (C) COLESOFT PA*
_ .+3C D9E3D5C5 D9E26B40 C9D5C34B 406040F2 F0F0F360 F2F0F1F1 4B40C1D3 D340D9C9 *RTNERS, INC. - 2003-2011. ALL RI*
_ .+5C C7C8E3E2 40D9C5E2 C5D9E5C5 C47A4040 40 *GHTS RESERVED: *
_ .+6D 00 0 *.*
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
_ .+72 181D LR R1,R13
_ .+74 41D0 F088 LA R13,X'088'(,R15)
_ .+78 50D0 1008 ST R13,X'008'(,R1)
_ .+7C 5010 D004 ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
_ .+88 SYMEDRSA 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 *................................*
_ .+A8 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 *................................*
_ .+C8 00000000 00000000 *........*
_ .+D0 47F0 D06C E0131END B X'06C'(,R13)
_ .+D4 @EXLST 0000E068 .EXLST *..\.*
_ .+D8 OLDIO EQU *
_ .+D8 56E0 D068 XAMODE31 O R14,X'068'(,R13)
_ .+DC 0B0E BSM 0,R14
_ .+DE 41E0 E000 ODCBX LA R14,X'000'(,R14)
_ .+E2 58F0 F00E L R15,X'00E'(,R15)
_ .+E6 0B0F BSM 0,R15
_ .+E8 EXLST 8500E05E FLMS7C.X#1+BB05E *e.\;*
Permanent and Transient Traps
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
_ .+72 181D LR R1,R13
_ .+74 41D0 F088 LA R13,X'088'(,R15)
_ .+78 50D0 1008 ST R13,X'008'(,R1)
_ .+7C 5010 D004 ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
A .+72 181D LR R1,R13
A .+74 41D0 F088 LA R13,X'088'(,R15)
T .+78 50D0 1008 ST R13,X'008'(,R1)
T .+7C 5010 D004 ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
_ .+72 001D AT00001A LR R1,R13
_ .+74 00D0 F088 AT00001B LA R13,X'088'(,R15)
_ .+78 00D0 1008 TR00001C ST R13,X'008'(,R1)
_ .+7C 0010 D004 TR00001D ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
_ .+72 001D AT00001A LR R1,R13
_ .+74 00D0 F088 AT00001B LA R13,X'088'(,R15)
_ .+78 00D0 1008 TR00001C ST R13,X'008'(,R1)
_ .+7C 0010 D004 TR00001D ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
_ .+72 001D AT00001A LR R1,R13
_ .+74 00D0 F088 AT00001B LA R13,X'088'(,R15)
_ .+78 00D0 1008 TR00001C ST R13,X'008'(,R1)
_ .+7C 0010 D004 TR00001D ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
Notes: Let’s get back to traps, both Permanent and Transient
<click1> I’m going to work with this snippet of code.
<click2> But let me enlarge it first so that we all can see what’s going on.
<click3> I’ll use some A and T shortcut commands to set some traps.
<click4> The A’s will set Permanent breakpoints.
<click5> The T’s will set a couple of transient breakpoints.
Now in real life, I probably would not set this sequence of breakpoints like this right here, I’m just doing this to illustrate some things.
<click6> So when I press ENTER, voila.
<click7> I have permanent breakpoints at offset 7-2 and 7-4.
<click8> And I have a couple of transients at 7-8 and seven charlie.
<click9> Notice also that the opcodes have been changed to zero-zeros.
<click10> Now take a look at the breakpoint names. Let me unpack them a bit.

## Slide 8
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
_ .+72 001D AT00001A LR R1,R13
_ .+74 00D0 F088 AT00001B LA R13,X'088'(,R15)
_ .+78 00D0 1008 TR00001C ST R13,X'008'(,R1)
_ .+7C 0010 D004 TR00001D ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
AT00001A
AT00001B
TR00001C
TR00001D
AT00001A
TR00001C
TR00001C
Type: AT or TRap
AT00001A
AT00001B
TR00001C
TR00001D
Type: AT or TRap
Family#
Do you notice how all FOUR of these breakpoint have been assigned to the same family? That’s because they were all created at the same time.
AT00001A
AT00001B
TR00001C
TR00001D
Type: AT or TRap
Family#
Uniqueness character
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
_ .+72 001D AT00001A LR R1,R13
_ .+74 41D0 F088 AT00001B LA R13,X'088'(,R15)
_ .+78 00D0 1008 TR00001C ST R13,X'008'(,R1)
_ .+7C 0010 D004 TR00001D ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
Permanent and Transient Traps
Notes: <implied click1>
<click2> The first part of each name identifies the breakpoint type: Permanent (AT) or Transient (TR).
<click3> The second part is the family number. Breakpoints in the same family can be removed collectively.
<click4> Do you notice how all four of these breakpoint have been assigned to the same family? That’s because they were all created at the same time.
<click5> The last part of each name is simply a uniqueness character.
<click6> That’s all…

## Slide 9
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------------------------------
XDC ===>
_ 00000000_0000DF80 8f (A.S.XDCDEMO) --- XDCSYMED.DBCSYMED+0, @R15+0, XDCSYMED+0, PRIVATE+BF80
_ .+0 >ENTRY EQU * DBCSYMED @CDP @R15
_ .+0 47F0 F06E >XDCSYMED B X'06E'(,R15) (.E0131ZID)
_ .+4 69 105 *.*
_ .+5 E0131MID C5D5E3D9 E840 *ENTRY *
_ .+B F1F061F1 F261F1F1 40 *10/12/11 *
_ .+14 F0F74BF5 F8406040 *07.58 - *
_ .+1C A961E7C4 C36B40C3 D6D7E8D9 C9C7C8E3 404DC35D 40C3D6D3 C5E2D6C6 E340D7C1 *z/XDC, COPYRIGHT (C) COLESOFT PA*
_ .+3C D9E3D5C5 D9E26B40 C9D5C34B 406040F2 F0F0F360 F2F0F1F1 4B40C1D3 D340D9C9 *RTNERS, INC. - 2003-2011. ALL RI*
_ .+5C C7C8E3E2 40D9C5E2 C5D9E5C5 C47A4040 40 *GHTS RESERVED: *
_ .+6D 00 0 *.*
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
_ .+72 001D AT00001A LR R1,R13
_ .+74 00D0 F088 AT00001B LA R13,X'088'(,R15)
_ .+78 00D0 1008 TR00001C ST R13,X'008'(,R1)
_ .+7C 0010 D004 TR00001D ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
_ .+88 SYMEDRSA 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 *................................*
_ .+A8 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 *................................*
_ .+C8 00000000 00000000 *........*
_ .+D0 47F0 D06C E0131END B X'06C'(,R13)
_ .+D4 @EXLST 0000E068 .EXLST *..\.*
_ .+D8 OLDIO EQU *
_ .+D8 56E0 D068 XAMODE31 O R14,X'068'(,R13)
_ .+DC 0B0E BSM 0,R14
_ .+DE 41E0 E000 ODCBX LA R14,X'000'(,R14)
_ .+E2 58F0 F00E L R15,X'00E'(,R15)
_ .+E6 0B0F BSM 0,R15
Permanent and Transient Traps
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------------------------------
XDC ===> GO
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------------------------------
XDC ===>
_ AT - LR
_ 00000000_0000DF80 8f (A.S.XDCDEMO) --- XDCSYMED.DBCSYMED+0, @R15+0, XDCSYMED+0, PRIVATE+BF80
_ .+0 ENTRY EQU * DBCSYMED @R15
_ .+0 47F0 F06E XDCSYMED B X'06E'(,R15)
_ .+4 69 105 *.*
_ .+5 E0131MID C5D5E3D9 E840 *ENTRY *
_ .+B F1F061F1 F261F1F1 40 *10/12/11 *
_ .+14 F0F74BF5 F8406040 *07.58 - *
_ .+1C A961E7C4 C36B40C3 D6D7E8D9 C9C7C8E3 404DC35D 40C3D6D3 C5E2D6C6 E340D7C1 *z/XDC, COPYRIGHT (C) COLESOFT PA*
_ .+3C D9E3D5C5 D9E26B40 C9D5C34B 406040F2 F0F0F360 F2F0F1F1 4B40C1D3 D340D9C9 *RTNERS, INC. - 2003-2011. ALL RI*
_ .+5C C7C8E3E2 40D9C5E2 C5D9E5C5 C47A4040 40 *GHTS RESERVED: *
_ .+6D 00 0 *.*
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
_ .+72 >AT00001A EQU *
_ .+72 001D >@CDP LR R1,R13
_ .+74 00D0 F088 AT00001B LA R13,X'088'(,R15)
_ .+78 50D0 1008 ST R13,X'008'(,R1)
_ .+7C 5010 D004 ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
_ .+88 SYMEDRSA 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 *................................*
_ .+A8 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 *................................*
_ .+C8 00000000 00000000 *........*
_ .+D0 47F0 D06C E0131END B X'06C'(,R13)
_ .+D4 @EXLST 0000E068 .EXLST *..\.*
_ .+D8 OLDIO EQU *
_ .+D8 56E0 D068 XAMODE31 O R14,X'068'(,R13)
_ .+DC 0B0E BSM 0,R14
_ .+DE 41E0 E000 ODCBX LA R14,X'000'(,R14)
_ .+E2 58F0 F00E L R15,X'00E'(,R15)
Notes: Ok, so what happens when execution reaches these breakpoints?
<click1> Let’s type a GO command and press ENTER.
<click2> Execution…
<click3> resumes at the branch at offset +0
<click4> and precedes to the AT-trap at offset 7-2.
[Flip back and forth once.]
Notice that the permanent breakpoints are still there,
<click5> BUT now the transients are gone!
Why is that?
Execution never reached them…
It was stopped by the first At-trap.
So why are they gone…

## Slide 10
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
_ .+72 001D AT00001A LR R1,R13
_ .+74 00D0 F088 AT00001B LA R13,X'088'(,R15)
_ .+78 00D0 1008 TR00001C ST R13,X'008'(,R1)
_ .+7C 0010 D004 TR00001D ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
When any breakpoint is reached by execution, all transient members of that family are automatically removed.
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
_ .+72 001D >AT00001A LR R1,R13
_ .+74 00D0 F088 AT00001B LA R13,X'088'(,R15)
_ .+78 00D0 1008 TR00001C ST R13,X'008'(,R1)
_ .+7C 0010 D004 TR00001D ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
_ .+6E 90EC D00C E0131ZID STM R14,R12,X'00C'(R13)
_ .+72 001D >AT00001A LR R1,R13
_ .+74 00D0 F088 AT00001B LA R13,X'088'(,R15)
_ .+78 50D0 1008 ST R13,X'008'(,R1)
_ .+7C 5010 D004 ST R1,X'004'(,R13)
_ .+80 5810 1018 L R1,X'018'(,R1)
_ .+84 47F0 D048 B X'048'(,R13)
Breakpoint Families
Notes: <implied click1>
<click2> Well, that’s because all of the breakpoints are in the same family.
<click3> And the rule is,
<click4> “When any breakpoint is reached by execution…
<click5> all transient members of that family are automatically removed.”

## Slide 11
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------------------------
XDC ===>
_ 00000000_12401014 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+5D4, @R14+28, XDCADATA+5D4,
_ XPRIVATE+1014
_ .+5D4 AFPRINTZ DS 0H 01/13 Z20 22270000
_ .+5D4 ************************************************************* 01/13 Z20 22420000
_ .+5D4 * Common First Call Processing -- Issue Hello World * 01/13 Z20 22430000
_ .+5D4 * messages. * 01/13 Z20 22440000
_ .+5D4 ************************************************************* 01/13 Z20 22460000
_ .+5D4 A718 03F7 LHI R1,MTITLE# TOKEN'TITLE LINE 01/13 Z20 22480000
_ .+5D8 A7E5 0C99 > JAS R14,MSGSEND SEND IT 02/13 Z20 22500000
_ .+5D8 A7E5 0C99 >@CDP JAS R14,*+X'1932' (.MSGSEND)
_ .+5DC 9610 D2FB OI AFTENV,AFTEATTN +0 ATTN RECEIVED, REMEMBER 01/13 Z20 22510000
_ .+5E0 ******** FALL THRU +4 PROCEED 01/13 Z20 22520000
_ .+5E0 A718 03EB LHI R1,MBLANK# TOKEN'BLANK LINE 01/13 Z20 22550000
_ .+5E4 A7E5 0C93 JAS R14,MSGSEND SEND IT 02/13 Z20 22560000
_ .+5E8 9610 D2FB OI AFTENV,AFTEATTN +0 ATTN RECEIVED, REMEMBER 01/13 Z20 22580000
_ .+5EC ******** FALL THRU +4 PROCEED 01/13 Z20 22590000
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------------------------
XDC ===>
_ 00000000_12401014 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+5D4, @R14+28, XDCADATA+5D4,
_ XPRIVATE+1014
_ .+5D4 AFPRINTZ DS 0H 01/13 Z20 22270000
_ .+5D4 ************************************************************* 01/13 Z20 22420000
_ .+5D4 * Common First Call Processing -- Issue Hello World * 01/13 Z20 22430000
_ .+5D4 * messages. * 01/13 Z20 22440000
_ .+5D4 ************************************************************* 01/13 Z20 22460000
_ .+5D4 A718 03F7 LHI R1,MTITLE# TOKEN'TITLE LINE 01/13 Z20 22480000
_ .+5D8 A7E5 0C99 > JAS R14,MSGSEND SEND IT 02/13 Z20 22500000
_ .+5D8 A7E5 0C99 >@CDP JAS R14,*+X'1932' (.MSGSEND)
_ .+5DC 9610 D2FB OI AFTENV,AFTEATTN +0 ATTN RECEIVED, REMEMBER 01/13 Z20 22510000
_ .+5E0 ******** FALL THRU +4 PROCEED 01/13 Z20 22520000
_ .+5E0 A718 03EB LHI R1,MBLANK# TOKEN'BLANK LINE 01/13 Z20 22550000
_ .+5E4 A7E5 0C93 JAS R14,MSGSEND SEND IT 02/13 Z20 22560000
_ .+5E8 9610 D2FB OI AFTENV,AFTEATTN +0 ATTN RECEIVED, REMEMBER 01/13 Z20 22580000
_ .+5EC ******** FALL THRU +4 PROCEED 01/13 Z20 22590000
Breakpoint Families
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------------------------
XDC ===>
_ 00000000_12401014 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+5D4, @R14+28, XDCADATA+5D4,
_ XPRIVATE+1014
_ .+5D4 AFPRINTZ DS 0H 01/13 Z20 22270000
_ .+5D4 ************************************************************* 01/13 Z20 22420000
_ .+5D4 * Common First Call Processing -- Issue Hello World * 01/13 Z20 22430000
_ .+5D4 * messages. * 01/13 Z20 22440000
_ .+5D4 ************************************************************* 01/13 Z20 22460000
_ .+5D4 A718 03F7 LHI R1,MTITLE# TOKEN'TITLE LINE 01/13 Z20 22480000
_ .+5D8 A7E5 0C99 > JAS R14,MSGSEND SEND IT 02/13 Z20 22500000
_ .+5D8 A7E5 0C99 >@CDP JAS R14,*+X'1932' (.MSGSEND)
T .+5DC 9610 D2FB OI AFTENV,AFTEATTN +0 ATTN RECEIVED, REMEMBER 01/13 Z20 22510000
_ .+5E0 ******** FALL THRU +4 PROCEED 01/13 Z20 22520000
T .+5E0 A718 03EB LHI R1,MBLANK# TOKEN'BLANK LINE 01/13 Z20 22550000
_ .+5E4 A7E5 0C93 JAS R14,MSGSEND SEND IT 02/13 Z20 22560000
_ .+5E8 9610 D2FB OI AFTENV,AFTEATTN +0 ATTN RECEIVED, REMEMBER 01/13 Z20 22580000
_ .+5EC ******** FALL THRU +4 PROCEED 01/13 Z20 22590000
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------------------------
XDC ===>
_ 00000000_12401014 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+5D4, @R14+28, XDCADATA+5D4,
_ XPRIVATE+1014
_ .+5D4 AFPRINTZ DS 0H 01/13 Z20 22270000
_ .+5D4 ************************************************************* 01/13 Z20 22420000
_ .+5D4 * Common First Call Processing -- Issue Hello World * 01/13 Z20 22430000
_ .+5D4 * messages. * 01/13 Z20 22440000
_ .+5D4 ************************************************************* 01/13 Z20 22460000
_ .+5D4 A718 03F7 LHI R1,MTITLE# TOKEN'TITLE LINE 01/13 Z20 22480000
_ .+5D8 A7E5 0C99 > JAS R14,MSGSEND SEND IT 02/13 Z20 22500000
_ .+5D8 A7E5 0C99 >@CDP JAS R14,*+X'1932' (.MSGSEND)
_ .+5DC 0010 D2FB TR00002B OI AFTENV,AFTEATTN +0 ATTN RECEIVED, REMEMBER 01/13 Z20 22510000
_ .+5E0 ******** FALL THRU +4 PROCEED 01/13 Z20 22520000
_ .+5E0 0018 03EB TR00002C LHI R1,MBLANK# TOKEN'BLANK LINE 01/13 Z20 22550000
_ .+5E4 A7E5 0C93 JAS R14,MSGSEND SEND IT 02/13 Z20 22560000
_ .+5E8 9610 D2FB OI AFTENV,AFTEATTN +0 ATTN RECEIVED, REMEMBER 01/13 Z20 22580000
_ .+5EC ******** FALL THRU +4 PROCEED 01/13 Z20 22590000
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------------------------
XDC ===> GO
_ 00000000_12401014 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+5D4, @R14+28, XDCADATA+5D4,
_ XPRIVATE+1014
_ .+5D4 AFPRINTZ DS 0H 01/13 Z20 22270000
_ .+5D4 ************************************************************* 01/13 Z20 22420000
_ .+5D4 * Common First Call Processing -- Issue Hello World * 01/13 Z20 22430000
_ .+5D4 * messages. * 01/13 Z20 22440000
_ .+5D4 ************************************************************* 01/13 Z20 22460000
_ .+5D4 A718 03F7 LHI R1,MTITLE# TOKEN'TITLE LINE 01/13 Z20 22480000
_ .+5D8 A7E5 0C99 > JAS R14,MSGSEND SEND IT 02/13 Z20 22500000
_ .+5D8 A7E5 0C99 >@CDP JAS R14,*+X'1932' (.MSGSEND)
_ .+5DC 0010 D2FB TR00002B OI AFTENV,AFTEATTN +0 ATTN RECEIVED, REMEMBER 01/13 Z20 22510000
_ .+5E0 ******** FALL THRU +4 PROCEED 01/13 Z20 22520000
_ .+5E0 0018 03EB TR00002C LHI R1,MBLANK# TOKEN'BLANK LINE 01/13 Z20 22550000
_ .+5E4 A7E5 0C93 JAS R14,MSGSEND SEND IT 02/13 Z20 22560000
_ .+5E8 9610 D2FB OI AFTENV,AFTEATTN +0 ATTN RECEIVED, REMEMBER 01/13 Z20 22580000
_ .+5EC ******** FALL THRU +4 PROCEED 01/13 Z20 22590000
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------------------------
XDC ===>
_ 00000000_12401014 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+5D4, @R14+28, XDCADATA+5D4,
_ XPRIVATE+1014
_ .+5D4 AFPRINTZ DS 0H 01/13 Z20 22270000
_ .+5D4 ************************************************************* 01/13 Z20 22420000
_ .+5D4 * Common First Call Processing -- Issue Hello World * 01/13 Z20 22430000
_ .+5D4 * messages. * 01/13 Z20 22440000
_ .+5D4 ************************************************************* 01/13 Z20 22460000
_ .+5D4 A718 03F7 LHI R1,MTITLE# TOKEN'TITLE LINE 01/13 Z20 22480000
_ .+5D8 A7E5 0C99 JAS R14,MSGSEND SEND IT 02/13 Z20 22500000
_ .+5DC 9610 D2FB OI AFTENV,AFTEATTN +0 ATTN RECEIVED, REMEMBER 01/13 Z20 22510000
_ .+5E0 >******** FALL THRU +4 PROCEED 01/13 Z20 22520000
_ .+5E0 A718 03EB > LHI R1,MBLANK# TOKEN'BLANK LINE 01/13 Z20 22550000
_ .+5E0 A718 03EB >@CDP LHI R1,X'03EB' (1003)
_ .+5E4 A7E5 0C93 JAS R14,MSGSEND SEND IT 02/13 Z20 22560000
_ .+5E8 9610 D2FB OI AFTENV,AFTEATTN +0 ATTN RECEIVED, REMEMBER 01/13 Z20 22580000
_ .+5EC ******** FALL THRU +4 PROCEED 01/13 Z20 22590000
Notes: So what good are breakpoint families? Here’s an example…
<click1> This code is about to jump-with-return to a subroutine named MSGSEND.
<click2> MSGSEND makes a vectored return. It might return to +0 or to +4.
I want to let MSGSEND run without stepping through it.
I just want to recapture execution when it returns,
But I don’t know which return it will make.
So the slow-motion solution is to…
<click3> use a couple of T shortcut commands
<click4> to set transient breakpoints onto both return points
<click5> and then type GO.
<click6> And it’s happened…
<Flip back and for the once> MSGSEND has executed…
<click7> and it has returned to offset +4.
Where execution was recaptured by z/XDC.
Now both transient breakpoints are no longer needed, so…
<click8> both transient breakpoints have been removed.
<click9> and both opcodes have been restored.

## Slide 12: Breakpoint Families
[fall thru]
X1
X2
X3
X4
TRAP X1 X2 X3 X4;GO
Notes: Here’s another example.
<click1> I’ve got a program here.
<click2> And it’s got a large loop…
You’ve stepped through it once or twice.
You know what it does.
It’s going to run though another couple of hundred thousand times.
You just want to let it run to completion,
And recapture execution when it finishes.
<click3> The problem is,
<click4> It’s got lotsa
<click5> way’s to finish.
<click6> Yes, it might fall through the bottom, but it also could easily jump out to several other places.
<click7> So what you’ve got to do is set breakpoints on each possible exit point.
And then type GO.
<click8> Here’s the command string that will do just that.
Since this command sets all the breakpoints at once, they are all assigned to the same family.
Since the TRAP command (not the AT command) is being used, all of the breakpoints are transient.

## Slide 13: Breakpoint Families
X4
[fall thru]
X1
X2
X3
TRAP X1 X2 X3 X4;GO
PSW
Notes: <implied click1> So when execution reaches any one of them, they ALL are automatically removed.

## Slide 14: Traces
Tracing is allowing the current one or more machine instructions to execute and recapturing execution upon a certain circumstance.
Let me explain what I mean by circumstance: z/XDC has 7 ways to trace execution:
  Single stepping (T): Allows one machine instruction to execute, and stops on the next.
  Branch tracing (T B): Steps from one branching instruction to the next.
  Successful branch tracing (T BY): Steps to the next branch instruction that will, in fact, branch. (The form that I use the most.)
  Unsuccessful branch tracing (T BN): Steps to the next branch instruction that will NOT actually branch. (A good way to get lost!)
  Loop Tracing (T *): Lets the current instruction execute and does not recapture execution until that instruction is executed again.
  Storage Alteration – Before (T SB): Stops on the next storage altering instruction before it executes.
  Storage Alteration – After (T SA): Stops just past the next storage altering instruction just after it executes.
Tracing is allowing the current one or more machine instructions to execute and recapturing execution upon a certain circumstance.
Let me explain what I mean by circumstance: z/XDC has 7 ways to trace execution:
  Single stepping (T): Allows one machine instruction to execute, and stops on the next.
  Branch tracing (T B): Steps from one branching instruction to the next.
  Successful branch tracing (T BY): Steps to the next branch instruction that will, in fact, branch. (The form that I use the most.)
  Unsuccessful branch tracing (T BN): Steps to the next branch instruction that will NOT actually branch. (A good way to get lost!)
  Loop Tracing (T *): Lets the current instruction execute and does not recapture execution until that instruction is executed again.
  Storage Alteration – Before (T SB): Stops on the next storage altering instruction before it executes.
  Storage Alteration – After (T SA): Stops just past the next storage altering instruction just after it executes.
Notes: Ok, so much for traps. Let’s turn our attention to Traces.
<click1> [Definition: read the slide]
<click2> [T: read the slide]
<click3> [T B: read the slide]
<click4> [T BY: read the slide]
<click5> [T BN: read the slide]
<click6> [T *: read the slide]
<click7> [T SB: read the slide]
<click8> [T SA: read the slide]
Now… Most of these trace types are pretty easy to understand, so I’m not going to go into excruciating detail about all of them… Just one!

## Slide 15: Traces – T BY
MBSINITZ LA R0...
JNZ MBSINITZ
JM MBSOOPS
MBIWDCBZ ICM R0...
JZ MBIWDCBZ
JZ MBIWDCBZ
(.MBIWDCBZ)
(NO BRANCH)
(.MBIWDCBZ)
T BY
(.MBSINITZ)
JNZ MBSINITZ
JZ MBIWDCBZ
XDC ===>
_ TRACE - JNZ (1 FALL THRU OCCURRED)
(.MBSINITZ)
JNZ MBSINITZ
(.MBSINITZ)
T BY
Notes: The T BY trace is pretty interesting. I think that in general it is the most useful. It stops only on successful branching instructions. So using T BY you can get through a chunk of code fairly quickly and when you’re done, you know EXACTLY what instructions have and have not been executed!
I’ll give an example.
<click1> Here’s my favorite program again.
<click2> Let me populate it with some code points…
<click3> And suppose execution has reached the JZ instruction.
Now when execution is at a branching instruction,
z/XDC will tell you whether or not it’s going to branch.
<click4> If it is going to branch, then z/XDC will show where it will branch to.
<click5> If it’s not going to branch, then z/XDC will show “(NO BRANCH)”.
<click6> In this case, it is going to branch.
<click7> So if I issue a T BY command, then…
<click8> the next thing you will see is execution stopped at the JNZ.
And then you will KNOW the following.
<click9> Execution resumed at the JZ and jumped to the ICM.
<click10> Everything from the JZ to the ICM was NOT executed. Guaranteed!
<click11> Everything from the ICM to the JNZ WAS executed. Guaranteed!
<click12> Every branching instruction between the ICM and the JNZ FELL THRU. Guaranteed!
<click13> In fact, z/XDC will even tell you how many fall thru’s occurred.
Now, the JNZ WILL in fact branch. Guaranteed!
<click14> And it will branch to MSBINITZ. Guaranteed!
All in all, T BY tracing tells you quite a bit of information…
<click15> Anyway, to continue, just wash. Rinse. Repeat.

## Slide 16: Hooks
z/XDC basically is a recovery routine. It can be used as an ESTAE, an ESTAEX, an ESTAI or even an FRR routine.
In order to use z/XDC to debug a section of code, two things must be true:
z/XDC must be the newest recovery routine for the code being debugged.
The retry level environment must be the same environment as that of the code being debugged… But what does this mean?
  If z/XDC is running as an ESTAE[X], then it must be owned by the Request Block (RB) under which the target code is running.
    One way for this to be true is if that code had issued an ESTAEX macro setting up z/XDC as its own recovery routine. (Fortunately, there are other ways to accomplish this.)
  If z/XDC is running as an ESTAI, then:
    The target code must be running under a Program Request Block (PRB),
    AND no older non-PRBs may exist on the Request Block chain.
When the above conditions are not met, then z/XDC cannot be used!
But hooks can fix that!
z/XDC basically is a recovery routine. It can be used as an ESTAE, an ESTAEX, an ESTAI or even an FRR routine.
In order to use z/XDC to debug a section of code, two things must be true:
z/XDC must be the newest recovery routine for the code being debugged.
The retry level environment must be the same environment as that of the code being debugged… But what does this mean?
  If z/XDC is running as an ESTAE[X], then it must be owned by the Request Block (RB) under which the target code is running.
    One way for this to be true is if that code had issued an ESTAEX macro setting up z/XDC as its own recovery routine. (Fortunately, there are other ways to accomplish this.)
  If z/XDC is running as an ESTAI, then:
    The target code must be running under a Program Request Block (PRB),
    AND no older non-PRBs may exist on the Request Block chain.
When the above conditions are not met, then z/XDC cannot be used!
But hooks can fix that!
Notes: <implied click> [Hide the text]
Read the slide for 12 clicks.

## Slide 17: Hooks
Hooking is setting a special kind of breakpoint, called a hook, that both captures execution and establishes z/XDC as the newest recovery routine (ESTAEX) for that point in your code. In other words, hooks set up the target code for debugging using z/XDC.
Hooks are implemented by setting an SVC instruction at the point where execution is to be intercepted and a z/XDC debugging session is to be established.
Generally you would use a Hook at a place in your code where a debugging session needs to be established, and then you would use Traps and Traces from then on for stepping through your code.
A z/XDC sessions needs to be established in any piece of code…
  that you want to debug
  and for which z/XDC is not yet the newest recovery routine (ESTAE[X] or ESTAI).
Hooking is setting a special kind of breakpoint, called a hook, that both captures execution and establishes z/XDC as the newest recovery routine (ESTAEX) for that point in your code. In other words, hooks set up the target code for debugging using z/XDC.
Hooks are implemented by setting an SVC instruction at the point where execution is to be intercepted and a z/XDC debugging session is to be established.
Generally you would use a Hook at a place in your code where a debugging session needs to be established, and then you would use Traps and Traces from then on for stepping through your code.
A z/XDC sessions needs to be established in any piece of code…
  that you want to debug
  and for which z/XDC is not yet the newest recovery routine (ESTAE[X] or ESTAI).
Notes: <implied click> [Hide the text]
Read the slide for 5 clicks.

## Slide 18: Hooks
...
SCB#5: ESTAE whatever4
PRB#2
[LINK]
SCB#6: ESTAEX SVC OPEN
SVRB#3 (OPEN)
[SVC OPEN]
PRB#4 (DCB OPEN exit)
[SVC SYNCH]
TCB#4 (XDCCALL)
[ATTACH]
PRB#1
TCB#5 (Yourpgm)
yourpgm
[ATTACH yourpgm
ESTAI=XDC]
(ownership)
SCB#1: ESTAI z/XDC
SCB#2: ESTAEX whatever
ESTAEX whatever
HOOK debugtarget
PSW
yourpgm
ESTAEX whatever
SCB#3: ESTAEX z/XDC
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------
XDC ===>
*FROMHOOK
. DBC830I XDC z1.13 ENTERED NONAUTHORIZED, AMODE(31), UNDER RB#3 FROM TCB#5 IN XDCDEMO2 (ASN=0032.2)
. DBC891I XDC z1.13 ENTERED AS AN ESTAEX OWNED BY RB#?
. DBC831I THE ERROR LEVEL AND RETRY LEVEL ENVIRONMENTS ARE THE SAME
_ TRACE - ICM
_ 00000000_12402A4E 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+200E, @R14+2E, XDCADATA+200E, XPRIVATE+2A4E
_ .+200E DIE8008Z EQU *
_ .+200E 1F22 MBSMGENZ SLR R2,R2
_ .+2010 >@CDP EQU *
_ .+2010 BF21 1000 >MBSPUTLP ICM R2,B'0001',X'000'(R1)
_ .+2014 A784 000A JZ *+X'0014' (.MBSAOK)
_ .+2018 A7E5 0058 JAS R14,*+X'00B0' (.PUTMSGS)
_ .+201C A7F4 000C J *+X'0018' (.MBSATTN)
Notes: Here’s a basic example:
<click1> Frequently, people start up their programs under XDCCALL.
<click2> And it ATTACH’s your program. In the process, the System builds a TCB and RB structure that looks something like this.
<click3> The ATTACH’s ESTAI= operand causes z/XDC to be defined as an ESTAI for the subtask structure.
<click4> Now suppose your program issues an ESTAEX to set up its own abend protection.
This creates an SCB that is newer than z/XDC’s SCB. Without Hooks, that means that z/XDC can no longer be used for debugging!
This is because when any abend occurs or any breakpoint is reached, the program’s recovery routine receives control first. The consequences of that almost always are disastrous and utterly confusing!
<click5> The solution to this problem is to use z/XDC’s HOOK command to set a hook into the code that you want to debug. Then type GO.
A hook is basically an SVC instruction and some control data (8 bytes total).
<click6> Eventually when execution reaches your hook point, one of z/XDC’s SVC routines gets control, and…
<click7> FIRST THING, he removes the hook!
<click8> Then he sets up z/XDC as the newest recovery routine (an ESTAEX in this case).
<click9> And he causes this ESTAEX to be owned by the Request Block under which the hooked code was running.
<click10> Finally, he passes control to z/XDC proper and you see a display.
You may note that the hook is gone, the hooked footprint has been restored, and execution is now positioned at the hook point.

## Slide 19: Hooks in SVC-Phobic Environments
Hooks are implemented via an SVC routine.
Therefore, they can only be used in code for which SVCs are legal.
Fortunately, for SRB code, FRR protected code, cross memory code etc. there is a hook script that can be used instead.
The script can be found in DBCOLE.XDCZ1D.XDCCMDS(SCRIPT).
Read its commentary for usage information.
See also HELP SCRIPTS HOOK.
Hooks are implemented via an SVC routine.
Therefore, they can only be used in code for which SVCs are legal.
Fortunately, for SRB code, FRR protected code, cross memory code etc. there is a hook script that can be used instead.
The script can be found in DBCOLE.XDCZ1D.XDCCMDS(HOOK).
Read its commentary for usage information.
See also HELP SCRIPTS HOOK.
Notes: <implied click> [Hide the text]
Read the slide for 5 clicks.

## Slide 20: Deferred Hooks and Traps
  A Deferred trap or hook is one that will be set only when the targeted load module is brought into storage (via LOAD, LINK, ATTACH[X] or XCTL).
  The ADEFERRED command sets deferred permanent traps.
  The TDEFERRED command sets deferred transient traps.
  The HDEFERRED command sets deferred hooks.
  Deferred traps/hooks can be set…
  Relative to a load module’s entry point.
  Relative to a load module’s starting address.
  Relative to any csect in the load module but only if a Binder map of the module has been pre-loaded (via the DMAP command).
  A Deferred trap or hook is one that will be set only when the targeted load module is brought into storage (via LOAD, LINK, ATTACH[X] or XCTL).
  The ADEFERRED command sets deferred permanent traps.
  The TDEFERRED command sets deferred transient traps.
  The HDEFERRED command sets deferred hooks.
  Deferred traps/hooks can be set…
  Relative to a load module’s entry point.
  Relative to a load module’s starting address.
  Relative to any csect in the load module but only if a Binder map of the module has been pre-loaded (via the DMAP command).
Notes: <implied click> [Hide the text]
Read the slide for 7 clicks.

## Slide 21: Setting a Deferred Trap Example
Load Module: XDCADATA
Csect: XDCADATA
Csect: DBCMSGEN
+8E BAKR R14,0
Notes: Here’s an example of setting a deferred breakpoint. I’m going to use the TDEFERRED command because I only expect the breakpoint to be needed for one hit.
<click1> Here’s a diagram of the target load module: In this case… XDCADATA.
The load module contains two csects.
<click2> The first is named XDCADATA.
<click3> The second is named DBCMSGEN.
<click4> There’s a BAKR in DBCMSGEN at offset +8E. That’s where I want to set my trap.

## Slide 22: Setting a Deferred Trap Example
TCB#9 RB#1 ------------------------------------------------- z/XDC ISPF INTERFACE -----------------------
XDC ===>
XDC ===> L MAPS
NO LOAD MODULES OR CSECTS ARE MAPPED
NO DSECTS ARE MAPPED
XDC ===> LIST BREAKPOINTS
DEFAULT CONDITIONAL - NONE
DEFAULT COMMANDS - NONE
TRACE DISPLAYS WILL BE ROLLED
NO BREAKPOINTS ARE DEFINED
TCB#9 RB#1 ------------------------------------------------- z/XDC ISPF INTERFACE -----------------------
XDC ===> dmap xdcadata.
READING THE DSECT MAP FOR XDCADATA FROM SYS1.CSW.LINKLIB(XDCADATA).
(READING ESD RECORDS FROM THE LOAD MODULE. METHOD=BSAM.)
The following maps have been built:
MAP TYPE LOCATION NAME
LOAD MODULE DSECT XDCADATA
XDC ===> L MAPS
NO LOAD MODULES OR CSECTS ARE MAPPED
THE FOLLOWING DSECTS ARE MAPPED
XDCADATA ------------- INACTIVE (000075C0)
XDC ===> LIST BREAKPOINTS
DEFAULT CONDITIONAL - NONE
DEFAULT COMMANDS - NONE
TRACE DISPLAYS WILL BE ROLLED
NO BREAKPOINTS ARE DEFINED
HELP COMMANDS DMAP CLONE
TCB#9 RB#1 ------------------------------------------------- z/XDC ISPF INTERFACE -----------------------
XDC ===>
READING THE DSECT MAP FOR XDCADATA FROM SYS1.CSW.LINKLIB(XDCADATA).
(READING ESD RECORDS FROM THE LOAD MODULE. METHOD=BSAM.)
The following maps have been built:
MAP TYPE LOCATION NAME
LOAD MODULE DSECT XDCADATA
XDC ===> L MAPS
NO LOAD MODULES OR CSECTS ARE MAPPED
THE FOLLOWING DSECTS ARE MAPPED
XDCADATA ------------- INACTIVE (000075C0)
XDC ===> LIST BREAKPOINTS
DEFAULT CONDITIONAL - NONE
DEFAULT COMMANDS - NONE
TRACE DISPLAYS WILL BE ROLLED
NO BREAKPOINTS ARE DEFINED
TCB#9 RB#1 ------------------------------------------------- z/XDC ISPF INTERFACE -----------------------
XDC ===> TD XDCADATA.DBCMSGEN+8E:LIST ALARM
READING THE DSECT MAP FOR XDCADATA FROM SYS1.CSW.LINKLIB(XDCADATA).
(READING ESD RECORDS FROM THE LOAD MODULE. METHOD=BSAM.)
The following maps have been built:
MAP TYPE LOCATION NAME
LOAD MODULE DSECT XDCADATA
XDC ===> L MAPS
NO LOAD MODULES OR CSECTS ARE MAPPED
THE FOLLOWING DSECTS ARE MAPPED
XDCADATA ------------- INACTIVE (000075C0)
XDC ===> LIST BREAKPOINTS
DEFAULT CONDITIONAL - NONE
DEFAULT COMMANDS - NONE
TRACE DISPLAYS WILL BE ROLLED
NO BREAKPOINTS ARE DEFINED
TCB#9 RB#1 ------------------------------------------------- z/XDC ISPF INTERFACE -----------------------
XDC ===> TD XDCADATA.DBCMSGEN+8E:LIST ALARM
READING THE DSECT MAP FOR XDCADATA FROM SYS1.CSW.LINKLIB(XDCADATA).
(READING ESD RECORDS FROM THE LOAD MODULE. METHOD=BSAM.)
The following maps have been built:
MAP TYPE LOCATION NAME
LOAD MODULE DSECT XDCADATA
XDC ===> L MAPS
NO LOAD MODULES OR CSECTS ARE MAPPED
THE FOLLOWING DSECTS ARE MAPPED
XDCADATA ------------- INACTIVE (000075C0)
XDC ===> LIST BREAKPOINTS
DEFAULT CONDITIONAL - NONE
DEFAULT COMMANDS - NONE
TRACE DISPLAYS WILL BE ROLLED
NO BREAKPOINTS ARE DEFINED
TCB#9 RB#1 ------------------------------------------------- z/XDC ISPF INTERFACE -----------------------
XDC ===> TD XDCADATA.DBCMSGEN+8E:LIST ALARM
READING THE DSECT MAP FOR XDCADATA FROM SYS1.CSW.LINKLIB(XDCADATA).
(READING ESD RECORDS FROM THE LOAD MODULE. METHOD=BSAM.)
The following maps have been built:
MAP TYPE LOCATION NAME
LOAD MODULE DSECT XDCADATA
XDC ===> L MAPS
NO LOAD MODULES OR CSECTS ARE MAPPED
THE FOLLOWING DSECTS ARE MAPPED
XDCADATA ------------- INACTIVE (000075C0)
XDC ===> LIST BREAKPOINTS
DEFAULT CONDITIONAL - NONE
DEFAULT COMMANDS - NONE
TRACE DISPLAYS WILL BE ROLLED
NO BREAKPOINTS ARE DEFINED
TCB#9 RB#1 ------------------------------------------------- z/XDC ISPF INTERFACE -----------------------
XDC ===>
XDC ===> L MAPS
NO LOAD MODULES OR CSECTS ARE MAPPED
THE FOLLOWING DSECTS ARE MAPPED
XDCADATA ------------- INACTIVE (000075C0)
XDC ===> LIST BREAKPOINTS
DEFAULT CONDITIONAL - NONE
DEFAULT COMMANDS - :LIST ALARM
TRACE DISPLAYS WILL BE ROLLED
THE FOLLOWING BREAKPOINTS ARE DEFINED:
_ TR00003C - DEFERRED (XDCADATA.X#1+41FE) ENABLED (0 CLONINGS)
:LIST ALARM
TCB#9 RB#1 ------------------------------------------------- z/XDC ISPF INTERFACE -----------------------
XDC ===>
XDC ===> L MAPS
NO LOAD MODULES OR CSECTS ARE MAPPED
THE FOLLOWING DSECTS ARE MAPPED
XDCADATA ------------- INACTIVE (000075C0)
XDC ===> LIST BREAKPOINTS
DEFAULT CONDITIONAL - NONE
DEFAULT COMMANDS - :LIST ALARM
TRACE DISPLAYS WILL BE ROLLED
THE FOLLOWING BREAKPOINTS ARE DEFINED:
_ TR00003C - DEFERRED (XDCADATA.X#1+41FE) ENABLED (0 CLONINGS)
:LIST ALARM
TCB#9 RB#1 ------------------------------------------------- z/XDC ISPF INTERFACE -----------------------
XDC ===> LOAD XDCADATA
XDC ===> L MAPS
NO LOAD MODULES OR CSECTS ARE MAPPED
THE FOLLOWING DSECTS ARE MAPPED
XDCADATA ------------- INACTIVE (000075C0)
XDC ===> LIST BREAKPOINTS
DEFAULT CONDITIONAL - NONE
DEFAULT COMMANDS - :LIST ALARM
TRACE DISPLAYS WILL BE ROLLED
THE FOLLOWING BREAKPOINTS ARE DEFINED:
_ TR00003C - DEFERRED (XDCADATA.X#1+41FE) ENABLED (0 CLONINGS)
:LIST ALARM
TCB#9 RB#1 ------------------------------------------------- z/XDC ISPF INTERFACE -----------------------
XDC ===> LOAD XDCADATA
ENTRY PRIMARY REFRNCE ENTRY USE SUB ATTRIBUTES
NAME NAME TCB/RB# ADDRESS COUNT POOL KEY (ATTR ATTR2 ATTR3-ATTRB)
_ XDCADATA 9 LLE 12647A40 1-0 251 8f 332042-30 RENT REUS PARTIAL_OR_NO_SPROT JPA PML_OK RACDTY CDEX CDE
ENTRY PRIMARY DFINING ENTRY USE SUB ATTRIBUTES
NAME NAME QUEUE ADDRESS COUNT POOL KEY (ATTR ATTR2 ATTR3-ATTRB)
_ XDCADATA JPQ-3 12647A40 1 251 8f 332042-30 RENT REUS PARTIAL_OR_NO_SPROT JPA PML_OK RACDTY CDEX CDE
XDC ===> L MAPS
NO LOAD MODULES OR CSECTS ARE MAPPED
THE FOLLOWING DSECTS ARE MAPPED
XDCADATA ------------- INACTIVE (000075C0)
XDC ===> LIST BREAKPOINTS
DEFAULT CONDITIONAL - NONE
DEFAULT COMMANDS - :LIST ALARM
TRACE DISPLAYS WILL BE ROLLED
THE FOLLOWING BREAKPOINTS ARE DEFINED:
_ TR00001A - DEFERRED (XDCADATA.X#1+41FE) ENABLED (1 CLONING)
:LIST ALARM
_ TR00001B - 1264BC3E (XDCADATA+41FE) ENABLED (0 HITS)
:LIST ALARM
TCB#9 RB#1 ------------------------------------------------- z/XDC ISPF INTERFACE -----------------------
XDC ===>
ENTRY PRIMARY REFRNCE ENTRY USE SUB ATTRIBUTES
NAME NAME TCB/RB# ADDRESS COUNT POOL KEY (ATTR ATTR2 ATTR3-ATTRB)
_ XDCADATA 9 LLE 12647A40 1-0 251 8f 332042-30 RENT REUS PARTIAL_OR_NO_SPROT JPA PML_OK RACDTY CDEX CDE
ENTRY PRIMARY DFINING ENTRY USE SUB ATTRIBUTES
NAME NAME QUEUE ADDRESS COUNT POOL KEY (ATTR ATTR2 ATTR3-ATTRB)
_ XDCADATA JPQ-3 12647A40 1 251 8f 332042-30 RENT REUS PARTIAL_OR_NO_SPROT JPA PML_OK RACDTY CDEX CDE
XDC ===> L MAPS
NO LOAD MODULES OR CSECTS ARE MAPPED
THE FOLLOWING DSECTS ARE MAPPED
XDCADATA ------------- INACTIVE (000075C0)
XDC ===> LIST BREAKPOINTS
DEFAULT CONDITIONAL - NONE
DEFAULT COMMANDS - :LIST ALARM
TRACE DISPLAYS WILL BE ROLLED
THE FOLLOWING BREAKPOINTS ARE DEFINED:
_ TR00001A - DEFERRED (XDCADATA.X#1+41FE) ENABLED (1 CLONING)
:LIST ALARM
_ TR00001B - 1264BC3E (XDCADATA+41FE) ENABLED (0 HITS)
:LIST ALARM
TCB#9 RB#1 ------------------------------------------------- z/XDC ISPF INTERFACE -----------------------
XDC ===>
ENTRY PRIMARY REFRNCE ENTRY USE SUB ATTRIBUTES
NAME NAME TCB/RB# ADDRESS COUNT POOL KEY (ATTR ATTR2 ATTR3-ATTRB)
_ XDCADATA 9 LLE 12647A40 1-0 251 8f 332042-30 RENT REUS PARTIAL_OR_NO_SPROT JPA PML_OK RACDTY CDEX CDE
ENTRY PRIMARY DFINING ENTRY USE SUB ATTRIBUTES
NAME NAME QUEUE ADDRESS COUNT POOL KEY (ATTR ATTR2 ATTR3-ATTRB)
_ XDCADATA JPQ-3 12647A40 1 251 8f 332042-30 RENT REUS PARTIAL_OR_NO_SPROT JPA PML_OK RACDTY CDEX CDE
XDC ===> L MAPS
NO LOAD MODULES OR CSECTS ARE MAPPED
THE FOLLOWING DSECTS ARE MAPPED
XDCADATA ------------- INACTIVE (000075C0)
XDC ===> LIST BREAKPOINTS
DEFAULT CONDITIONAL - NONE
DEFAULT COMMANDS - :LIST ALARM
TRACE DISPLAYS WILL BE ROLLED
THE FOLLOWING BREAKPOINTS ARE DEFINED:
_ TR00001A - DEFERRED (XDCADATA.X#1+41FE) ENABLED (1 CLONING)
:LIST ALARM
F TR00001B - 1264BC3E (XDCADATA+41FE) ENABLED (0 HITS)
:LIST ALARM
TCB#9 RB#1 ------------------------------------------------- z/XDC ISPF INTERFACE --------------------------
XDC ===>
_ 00000000_1264BC3E 8f (A.S.DBCOLE3) --- XDCADATA+41FE, XPRIVATE+24BC3E
_ +41FE TR00001B EQU *
_ +41FE 0040 00E0 @CDP BAKR R14,0
_ +4202 B219 0000 SAC B'0000XXXXXXXX'
_ +4206 010D SAM31 ,
_ +4208 90EC D00C STM R14,R12,X'00C'(R13)
_ +420C C0C0 0000 1446 LARL R12,*+X'0000288C' (XDCADATA+6A98)
_ +4212 D203 D000 C028 MVC X'000'(4,R13),X'028'(R12)
_ +4218 18B1 LR R11,R1
_ +421A 1FAA SLR R10,R10
_ +421C 1F99 SLR R9,R9
_ +421E A738 0330 LHI R3,X'0330' (816)
_ +4222 0D20 BASR R2,0
_ +4224 47F0 2008 B X'008'(,R2)
_ +4228 4800 8370 LH R0,X'370'(,R8)
_ +422C 1803 LR R0,R3
_ +422E 58F0 2004 L R15,X'004'(,R2)
_ +4232 58E0 0010 L R14,X'010'
_ +4236 58EE 0304 L R14,X'304'(R14)
_ +423A 58EE 00A0 L R14,X'0A0'(R14)
_ +423E B218 E000 PC X'000'(R14)
_ +4242 1811 LR R1,R1
_ +4244 A7FE 0014 CHI R15,X'0014' (20)
_ +4248 A784 0008 JE *+X'0010' (XDCADATA+4258)
_ +424C 1803 LR R0,R3
_ +424E 12FF LTR R15,R15
_ +4250 A774 125D JNZ *+X'24BA' (XDCADATA+670A)
_ +4254 1821 LR R2,R1
_ +4256 0E2E MVCL R2,R14
Notes: We’ll start of with nothing.
<click1> I’m going to start by pre-loading a Binder map of the XDCADATA load module.
This done using the DMAP command.
Normally, the DMAP command loads dsect maps.
But it can also be used to load both CSECT maps and Binder maps as if they were dsects.
<click2> For Binder maps, the lone period following the load module name is what tells the DMAP command what is wanted. (yeah, there’s an explanation, but… oh never mind.)
<click3> For more information, see HELP COMMANDS DMAP CLONE.
<click4>
<click5> This is the TDEFERRED command I’m going to issue.
<click6> The fact that I’ve preloaded the Binder map
<click7> is what allows its address expression to reference a csect within the load module.
<click8>
<click9> For the hell of it, I have assigned a command string that will be executed once a live breakpoint has been set and then reached by program execution.
(The LIST ALARM command will cause your terminal to beep. Not because that’s what it does, but because it’s an illegal command.)
<click10>
Anyway, let’s press ENTER…<click11>
<click12> And a deferred breakpoint template has been created.
So the next time XDCADATA is loaded by the current debugging session, a transient breakpoint will be inserted into it during the load process.
<click13> To illustrate, <click14> I’ll force a load right now.
<click15> Notice that the template has been cloned.
<click16> And that a new breakpoint has been created.
<click17> Now if I use an F shortcut command,
<click18> I’ll see the code into which the breakpoint was set.

## Slide 23: Conditional Traps
Traps and Traces can be Conditional: They will not “be accepted” until a specified condition resolves TRUE:
Counting Conditions: The trap must be reach n number of times.
Boolean Expressions: Tests values in registers and/or storage.
Traps and Traces can be Conditional: They will not “be accepted” until a specified condition resolves TRUE:
Counting Conditions: The trap must be reach n number of times.
Boolean Expressions: Tests values in registers and/or storage.
Notes: <implied click> [Hide the text]
Read the slide for 3 clicks.

## Slide 24: Conditional Traps - Counting
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------
XDC ===>
_ 00000000_12401718 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+CD8, @R15+CD8, XDCADATA+CD8,
_ XPRIVATE+1718
_ .+CD8 @CDP EQU *
_ .+CD8 50F0 B030 AGOTADAT ST R15,X'030'(,R11)
_ .+CDC B916 000F LLGFR RW0,R15
_ .+CE0 B91B 0006 SLGFR RW0,R6
_ .+CE4 5500 B1B8 CL R0,X'1B8'(,R11)
_ .+CE8 A7D4 0004 JNH *+X'0008' (.AMAXADIZ)
_ .+CEC 5000 B1B8 ST R0,X'1B8'(,R11)
_ .+CF0 E300 B178 000A AMAXADIZ ALG RW0,X'00178'(,R11)
XDC ===> l breakpoints
DEFAULT CONDITIONAL - NONE
DEFAULT COMMANDS - NONE
TRACE DISPLAYS WILL BE ROLLED
NO BREAKPOINTS ARE DEFINED
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------
XDC ===> t +0 (375);f +0
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------
XDC ===> t +0 (375);f +0
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------
XDC ===> t +0 (375);f +0
_ 00000000_12401718 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+CD8, @R15+CD8, XDCADATA+CD8,
_ XPRIVATE+1718
_ .+CD8 @CDP EQU * TR00004D
_ .+CD8 00F0 B030 AGOTADAT ST R15,X'030'(,R11)
_ .+CDC B916 000F LLGFR RW0,R15
_ .+CE0 B91B 0006 SLGFR RW0,R6
_ .+CE4 5500 B1B8 CL R0,X'1B8'(,R11)
_ .+CE8 A7D4 0004 JNH *+X'0008' (.AMAXADIZ)
_ .+CEC 5000 B1B8 ST R0,X'1B8'(,R11)
_ .+CF0 E300 B178 000A AMAXADIZ ALG RW0,X'00178'(,R11)
XDC ===> l breakpoints
DEFAULT CONDITIONAL - (375)
DEFAULT COMMANDS - NONE
TRACE DISPLAYS WILL BE ROLLED
THE FOLLOWING BREAKPOINTS ARE DEFINED:
_ TR00004D - 12401718 (.AGOTADAT) ENABLED (0 HITS)
(375)
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------
XDC ===> GO
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------
XDC ===>
_ TRACE - ST (374 FALSE CONDITIONS)
_ 00000000_12401718 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+CD8, @R15+CD8, XDCADATA+CD8,
_ XPRIVATE+1718
_ .+CD8 >@CDP EQU *
_ .+CD8 50F0 B030 >AGOTADAT ST R15,X'030'(,R11)
_ .+CDC B916 000F LLGFR RW0,R15
_ .+CE0 B91B 0006 SLGFR RW0,R6
_ .+CE4 5500 B1B8 CL R0,X'1B8'(,R11)
_ .+CE8 A7D4 0004 JNH *+X'0008' (.AMAXADIZ)
_ .+CEC 5000 B1B8 ST R0,X'1B8'(,R11)
XDC ===> l breakpoints
DEFAULT CONDITIONAL - (375)
DEFAULT COMMANDS - NONE
TRACE DISPLAYS WILL BE ROLLED
NO BREAKPOINTS ARE DEFINED
Notes: <click1> I’m going to illustrate using a counting conditional trap.
<click2> A-GOTTA-DAT is a critical loop point in my program.
Previously, I’ve figured out that I’ve got a problem handling the 375th ADATA record processed through this point.
<click3> So I’ll set a trap that will not be accepted until it has been reached by execution <click4> the 375th time.
<click5> Pressing ENTER…
<click6> The trap is now set, and the code is redisplayed showing it.
<click7> Note, in this case, I had to use the primary TRAP command, not just the T shortcut.
<click8> So now I’ll type GO, and let the program do its thing…
<click9> 375 times. And here’s the result…
<click10> Execution has stopped at A-GOTTA-DAT.
<click11> 374 times, execution went through here without stopping.
<click12> The breakpoint has been removed,
<click13> and the STore instruction's original opcode has been restored.

## Slide 25: Conditional Traps - Boolean
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------
XDC ===>
_ 00000000_12401804 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+DC4, @R14+3BA, XDCADATA+DC4,
_ XPRIVATE+1804
_ .+DC4 @CDP EQU *
_ .+DC4 4110 6000 ADAT0030 LA R1,X'000'(,R6)
_ .+DC8 A7E5 0754 JAS R14,*+X'0EA8' (.A30FILTR)
_ .+DCC A7F4 FFB4 J *-X'0098' (.AFREJCNT)
_ .+DD0 BF1F 6078 ICM R1,B'1111',X'078'(R6)
_ .+DD4 A7D4 006C JNP *+X'00D8' (.ADAT0036)
_ .+DD8 5A10 6040 A R1,X'040'(,R6)
XDC ===> f abuffer
_ 00000000_1316F000 8f (A.S.XDCDEMO2) --- ABUFFER+0, @R6+0, XPRIVATE+D6F000
_ +0 @CDP @R6
_ +0 ABUFFER 10 16 *.*
_ +1 ARECTYPE 0030 +48 *..*
_ +3 03000100 000000 *.......*
_ +A ADATALEN 00DC +220 *..*
_ +C AHEADERZ FFFFFFFE 7FFFFFFE *....*
_ +10 ADSRCSTMT
_ +10 00000137 +311 *....*
XDC ===> l breakpoints
DEFAULT CONDITIONAL - (375)
DEFAULT COMMANDS - NONE
TRACE DISPLAYS WILL BE ROLLED
NO BREAKPOINTS ARE DEFINED
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------
XDC ===>
_ 00000000_12401804 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+DC4, @R14+3BA, XDCADATA+DC4,
_ XPRIVATE+1804
_ .+DC4 @CDP EQU *
_ .+DC4 4110 6000 ADAT0030 LA R1,X'000'(,R6)
_ .+DC8 A7E5 0754 JAS R14,*+X'0EA8' (.A30FILTR)
_ .+DCC A7F4 FFB4 J *-X'0098' (.AFREJCNT)
_ .+DD0 BF1F 6078 ICM R1,B'1111',X'078'(R6)
_ .+DD4 A7D4 006C JNP *+X'00D8' (.ADAT0036)
_ .+DD8 5A10 6040 A R1,X'040'(,R6)
XDC ===> f abuffer
_ 00000000_1316F000 8f (A.S.XDCDEMO2) --- ABUFFER+0, @R6+0, XPRIVATE+D6F000
_ +0 @CDP @R6
_ +0 ABUFFER 10 16 *.*
_ +1 ARECTYPE 0030 +48 *..*
_ +3 03000100 000000 *.......*
_ +A ADATALEN 00DC +220 *..*
_ +C AHEADERZ FFFFFFFE 7FFFFFFE *....*
_ +10 ADSRCSTMT
_ +10 00000137 +311 *....*
XDC ===> l breakpoints
DEFAULT CONDITIONAL - (375)
DEFAULT COMMANDS - NONE
TRACE DISPLAYS WILL BE ROLLED
NO BREAKPOINTS ARE DEFINED
Notes: <click1> Now to show boolean conditional traps.
This is a program that processes ADATA records.
<click2> I’ve created a set of floating equates to lay out fields of particular interest in my ADATA buffer.
(Sometimes I prefer to use equates and forgo the clutter of full blown dsect maps.)
I’ve got a problem with my program’s handling of a particular type 0030 record.
(Thirties are for program source images.)
<click3> Here is the code that handles those records.

## Slide 26: Conditional Traps - Boolean
20376 ************************************************************* 01/13 Z20
20377 * PUTLINE Support Area * 01/13 Z20
20378 ************************************************************* 01/13 Z20
0000014C 20380 P31PUTL@ DS A @'IKJPUTL 01/13 Z20
20382 P31PTPB PUTLINE OUTPUT=(AFTMSGBF-4, @'OUTPUT LINE 01/13 Z20*
TERM, SEND THE MESSAGE(S) 01/13 Z20*
SINGLE, ONLY ONE MSG AT A TIME 01/13 Z20*
DATA), IT'S JUST LUNCH 01/13 Z20*
TERMPUT=(EDIT, DO FULL MSG SETUP EDITING 01/13 Z20*
WAIT, INSURE THE MSG IS BUFFERED 01/13 Z20*
NOHOLD), DON'T WAIT FOR ACTUAL DISPLAY 13 Z20*
MF=L LIST FORM 01/13 Z20
00000150 20383+ DS 0F
00000150 30 20384+P31PTPB DC B'00110000' SET CONTROL FIELD
00000151 00 20385+ DC B'00000000' SET CONTROL FIELD @E22D2DA
00000152 00 20386+ DC B'00000000' SET TOUTPUT OPTIONS FIELD
00000153 00 20387+ DC X'00' SET TOUTPUT OPTIONS FIELD
00000154 00000440 20388+ DC A(AFTMSGBF-4) ADDR OF OUTPUT LINE
00000158 00000000 20389+ DC A(0) ADDRESS OF FORMATTED LINE
0000000C 20390 P31PTPBL EQU *-P31PTPB L'PBLOCK 01/13 Z20
0000015C 20392 DS 0F | ALIGNMENT 01/13 Z20
0000015C 20393 P31IOPL DS XL(IOPLLEN) V IOPL BUFFER 01/13 Z20
Notes: <Implied click1> Here’s the problem area in my source listing.
<click2> The problem statement is number 20-3-82

## Slide 27: Conditional Traps - Boolean
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------
XDC ===>
_ 00000000_12401804 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+DC4, @R14+3BA, XDCADATA+DC4,
_ XPRIVATE+1804
_ .+DC4 @CDP EQU *
_ .+DC4 4110 6000 ADAT0030 LA R1,X'000'(,R6)
_ .+DC8 A7E5 0754 JAS R14,*+X'0EA8' (.A30FILTR)
_ .+DCC A7F4 FFB4 J *-X'0098' (.AFREJCNT)
_ .+DD0 BF1F 6078 ICM R1,B'1111',X'078'(R6)
_ .+DD4 A7D4 006C JNP *+X'00D8' (.ADAT0036)
_ .+DD8 5A10 6040 A R1,X'040'(,R6)
XDC ===> f abuffer
_ 00000000_1316F000 8f (A.S.XDCDEMO2) --- ABUFFER+0, @R6+0, XPRIVATE+D6F000
_ +0 @CDP @R6
_ +0 ABUFFER 10 16 *.*
_ +1 ARECTYPE 0030 +48 *..*
_ +3 03000100 000000 *.......*
_ +A ADATALEN 00DC +220 *..*
_ +C AHEADERZ FFFFFFFE 7FFFFFFE *....*
_ +10 ADSRCSTMT
_ +10 00000137 +311 *....*
XDC ===> l breakpoints
DEFAULT CONDITIONAL - (375)
DEFAULT COMMANDS - NONE
TRACE DISPLAYS WILL BE ROLLED
NO BREAKPOINTS ARE DEFINED
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------
XDC ===> t +0 (adsrcstmt,ge,00004f9e):l alarm;f +0
t +0 (adsrcstmt,ge,00004f9e):l alarm;f +0
This is the target address for the breakpoint.
+0 is z/XDC’s way of saying, “right here”.
More formally, the implied base of the given offset is z/XDC’s “Current Display Pointer”.
(That’s what the @CDP equate is all about.)
t +0 (adsrcstmt,ge,00004f9e):l alarm;f +0
This is the conditional expression.
Generally, it is in the form of (location,relation,hexstring).
Location may be storage, register or PSW.
The expression may be compounded.
00004f9e is the hex equivalent of 20,382 decimal.
The number of hex digits determines the width of the comparison.
t +0 (adsrcstmt,ge,00004f9e):l alarm;f +0
This is the command string to be executed when the breakpoint is reached by execution and the conditional expression resolves TRUE.
The string may contain any number of commands, but each command must be led by a colon (:).
A semicolon (;) or end-of-command ends the command string.
L ALARM will cause your terminal to beep (not because that’s what it does, but because L ALARM is not a legal command.)
t +0 (adsrcstmt,ge,00004f9e):l alarm;f +0
This command string is not saved for later execution by the breakpoint. Instead, it is executed immediately.
That’s because it is led by a semicolon (;), not a colon (:).
It’s purpose is to cause a redisplay so that the breakpoint can be seen.
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ----------
XDC ===> t +0 (adsrcstmt,ge,00004f9e):l alarm;f +0
_ 00000000_12401804 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+DC4, @R14+3BA, XDCADATA+DC4,
_ XPRIVATE+1804
_ .+DC4 @CDP EQU *
_ .+DC4 4110 6000 ADAT0030 LA R1,X'000'(,R6)
_ .+DC8 A7E5 0754 JAS R14,*+X'0EA8' (.A30FILTR)
_ .+DCC A7F4 FFB4 J *-X'0098' (.AFREJCNT)
_ .+DD0 BF1F 6078 ICM R1,B'1111',X'078'(R6)
_ .+DD4 A7D4 006C JNP *+X'00D8' (.ADAT0036)
_ .+DD8 5A10 6040 A R1,X'040'(,R6)
XDC ===> f abuffer
_ 00000000_1316F000 8f (A.S.XDCDEMO2) --- ABUFFER+0, @R6+0, XPRIVATE+D6F000
_ +0 @CDP @R6
_ +0 ABUFFER 10 16 *.*
_ +1 ARECTYPE 0030 +48 *..*
_ +3 03000100 000000 *.......*
_ +A ADATALEN 00DC +220 *..*
_ +C AHEADERZ FFFFFFFE 7FFFFFFE *....*
_ +10 ADSRCSTMT
_ +10 00000137 +311 *....*
XDC ===> l breakpoints
DEFAULT CONDITIONAL - (375)
DEFAULT COMMANDS - NONE
TRACE DISPLAYS WILL BE ROLLED
NO BREAKPOINTS ARE DEFINED
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------
XDC ===>
_ 00000000_12401804 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+DC4, @R14+3BA, XDCADATA+DC4,
_ XPRIVATE+1804
_ .+DC4 @CDP EQU * TR00005E
_ .+DC4 0010 6000 ADAT0030 LA R1,X'000'(,R6)
_ .+DC8 A7E5 0754 JAS R14,*+X'0EA8' (.A30FILTR)
_ .+DCC A7F4 FFB4 J *-X'0098' (.AFREJCNT)
_ .+DD0 BF1F 6078 ICM R1,B'1111',X'078'(R6)
_ .+DD4 A7D4 006C JNP *+X'00D8' (.ADAT0036)
_ .+DD8 5A10 6040 A R1,X'040'(,R6)
XDC ===> f abuffer
_ 00000000_1316F000 8f (A.S.XDCDEMO2) --- ABUFFER+0, @R6+0, XPRIVATE+D6F000
_ +0 @CDP @R6
_ +0 ABUFFER 10 16 *.*
_ +1 ARECTYPE 0030 +48 *..*
_ +3 03000100 000000 *.......*
_ +A ADATALEN 00DC +220 *..*
_ +C AHEADERZ FFFFFFFE 7FFFFFFE *....*
_ +10 ADSRCSTMT
_ +10 00000137 +311 *....*
XDC ===> l breakpoints
DEFAULT CONDITIONAL - (adsrcstmt,ge,00004f9e)
DEFAULT COMMANDS - :l alarm
TRACE DISPLAYS WILL BE ROLLED
THE FOLLOWING BREAKPOINTS ARE DEFINED:
_ TR00005E - 12401804 (.ADAT0030) ENABLED (0 HITS)
(adsrcstmt,ge,00004f9e) :l alarm
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------
XDC ===> t +0 (adsrcstmt,ge,00004f9e):l alarm;f +0
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------
XDC ===> t +0 (adsrcstmt,ge,00004f9e):l alarm;f +0
_ 00000000_12401804 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+DC4, @R14+3BA, XDCADATA+DC4,
_ XPRIVATE+1804
_ .+DC4 @CDP EQU * TR00005E
_ .+DC4 0010 6000 ADAT0030 LA R1,X'000'(,R6)
_ .+DC8 A7E5 0754 JAS R14,*+X'0EA8' (.A30FILTR)
_ .+DCC A7F4 FFB4 J *-X'0098' (.AFREJCNT)
_ .+DD0 BF1F 6078 ICM R1,B'1111',X'078'(R6)
_ .+DD4 A7D4 006C JNP *+X'00D8' (.ADAT0036)
_ .+DD8 5A10 6040 A R1,X'040'(,R6)
XDC ===> f abuffer
_ 00000000_1316F000 8f (A.S.XDCDEMO2) --- ABUFFER+0, @R6+0, XPRIVATE+D6F000
_ +0 @CDP @R6
_ +0 ABUFFER 10 16 *.*
_ +1 ARECTYPE 0030 +48 *..*
_ +3 03000100 000000 *.......*
_ +A ADATALEN 00DC +220 *..*
_ +C AHEADERZ FFFFFFFE 7FFFFFFE *....*
_ +10 ADSRCSTMT
_ +10 00000137 +311 *....*
XDC ===> l breakpoints
DEFAULT CONDITIONAL - (adsrcstmt,ge,00004f9e)
DEFAULT COMMANDS - :l alarm
TRACE DISPLAYS WILL BE ROLLED
THE FOLLOWING BREAKPOINTS ARE DEFINED:
_ TR00005E - 12401804 (.ADAT0030) ENABLED (0 HITS)
(adsrcstmt,ge,00004f9e) :l alarm
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------
XDC ===> GO
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------
XDC ===>
_ TRACE - LA (1,076 FALSE CONDITIONS)
>>> L alarm <<<
L ALARM
*
. DBC062E WORD NOT RECOGNIZED
22 - S BK O AT00003C
XDC ===> f abuffer
_ 00000000_1316F000 8f (A.S.XDCDEMO2) --- ABUFFER+0, @R6+0, XPRIVATE+D6F000
_ +0 @CDP @R6
_ +0 ABUFFER 10 16 *.*
_ +1 ARECTYPE 0030 +48 *..*
_ +3 03000100 000000 *.......*
_ +A ADATALEN 00D4 +212 *.M*
_ +C AHEADERZ FFFFFF87 7FFFFF87 *...g*
_ +10 ADSRCSTMT
_ +10 00004F9E +20382 *....*
XDC ===> l breakpoints
DEFAULT CONDITIONAL - (adsrcstmt,ge,00004f9e)
DEFAULT COMMANDS - :l alarm
TRACE DISPLAYS WILL BE ROLLED
THE FOLLOWING BREAKPOINTS ARE DEFINED:
_ TR00005E - 12401804 (.ADAT0030) DISABLED NOT-SET (1 HIT, 1,076 FALSE CONDITIONS)
(adsrcstmt,ge,00004f9e) :l alarm
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------
XDC ===>
_ TRACE - LA (1,076 FALSE CONDITIONS)
>>> L alarm <<<
L ALARM
*
. DBC062E WORD NOT RECOGNIZED
22 - S BK O AT00003C
XDC ===> f abuffer
_ 00000000_1316F000 8f (A.S.XDCDEMO2) --- ABUFFER+0, @R6+0, XPRIVATE+D6F000
_ +0 @CDP @R6
_ +0 ABUFFER 10 16 *.*
_ +1 ARECTYPE 0030 +48 *..*
_ +3 03000100 000000 *.......*
_ +A ADATALEN 00D4 +212 *.M*
_ +C AHEADERZ FFFFFF87 7FFFFF87 *...g*
_ +10 ADSRCSTMT
_ +10 00004F9E +20382 *....*
XDC ===> l breakpoints
DEFAULT CONDITIONAL - (adsrcstmt,ge,00004f9e)
DEFAULT COMMANDS - :l alarm
TRACE DISPLAYS WILL BE ROLLED
THE FOLLOWING BREAKPOINTS ARE DEFINED:
_ TR00005E - 12401804 (.ADAT0030) DISABLED NOT-SET (1 HIT, 1,076 FALSE CONDITIONS)
(adsrcstmt,ge,00004f9e) :l alarm
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE ---------------------
XDC ===> WHERE
_ 00000000_12401804 8f (A.S.XDCDEMO2) --- XDCADATA.XDCADATA+DC4, @R15+0, @R14+B0, XDCADATA+DC4,
_ XPRIVATE+1804
_ .+DC4 >@CDP EQU * @R15 TR00002B
_ .+DC4 4110 6000 >ADAT0030 LA R1,X'000'(,R6)
_ .+DC8 A7E5 0754 JAS R14,*+X'0EA8' (.A30FILTR)
_ .+DCC A7F4 FFB4 J *-X'0098' (.AFREJCNT)
_ .+DD0 BF1F 6078 ICM R1,B'1111',X'078'(R6)
_ .+DD4 A7D4 006C JNP *+X'00D8' (.ADAT0036)
_ .+DD8 5A10 6040 A R1,X'040'(,R6)
XDC ===> f abuffer
_ 00000000_1316F000 8f (A.S.XDCDEMO2) --- ABUFFER+0, @R6+0, XPRIVATE+D6F000
_ +0 @CDP @R6
_ +0 ABUFFER 10 16 *.*
_ +1 ARECTYPE 0030 +48 *..*
_ +3 03000100 000000 *.......*
_ +A ADATALEN 00D4 +212 *.M*
_ +C AHEADERZ FFFFFF87 7FFFFF87 *...g*
_ +10 ADSRCSTMT
_ +10 00004F9E +20382 *....*
XDC ===> l breakpoints
DEFAULT CONDITIONAL - (adsrcstmt,ge,00004f9e)
DEFAULT COMMANDS - :l alarm
TRACE DISPLAYS WILL BE ROLLED
THE FOLLOWING BREAKPOINTS ARE DEFINED:
_ TR00005E - 12401804 (.ADAT0030) DISABLED NOT-SET (1 HIT, 1,076 FALSE CONDITIONS)
(adsrcstmt,ge,00004f9e) :l alarm
Notes: <Implied click1> Getting back to my program…
<click1> I want to set a conditional trap at ADAT0030 that doesn’t fire until statement # 20-3-82 comes walking in the door.
<click2> Here’s the command string I’m going to use.
<click3> But before I press ENTER, let me unpack this a bit.
<click4> [+0: read the slide]
<click5> [(x,ge,y): read the slide]
<click6> [l alarm: read the slide]
<click7> [f +0: read the slide]
<click8> Ok, let’s get on with it.
<click9> So now I’ll press ENTER, and the trap gets set.
<click10> Now I’ll issue a GO and let-er-rip.
It takes a moment, but eventually
<click11> The ADATA 0030 record from listing statement # 20-3-82 was reached,
So the conditional expression resolved TRUE.
So the breakpoint was finally accepted and the program stopped.
And now you can see the display.
<click12> This mess happened, because as I said earlier, LIST ALARM is not really a legal command. BUT… the terminal did beep! []
<click13> Now a WHERE command shows me where I am, and I am now ready to go traipsing off looking for my problem with record 20-3-82.

## Slide 28: Last Page
TCB#5 RB#1 -------------------------------------------------XDC-CDF ISPF INTERFACE -------------------------------------
XDC ===> Any Questions?
XDC ===> L PSW;L EPSW;L RWREGS;;L AREGS
_ PSW 078D0000 92D03718 (cc-EQ) (31) - .AGOTADAT
_ EPSW 078D0000 92D0371A (cc-EQ) (31) - .XDCADATA.+CDA
_ RW0 00000000_000000D4 00000000_0000E0B8 FFFFFFFF_131D70E0 FFFFFFFF_000000E0 *.......M......\........\.......\*
_ RW4 FFFFFFFF_0005D074 FFFFFFFF_00000000 FFFFFFFF_131D7000 FFFFFFFF_92402B52 *......}.....................k ..*
_ RW8 FFFFFFFF_0003BAB0 FFFFFFFF_0003BA94 FFFFFFFF_0000E0B8 FFFFFFFF_12472170 *...............m......\.........*
_ RW12 FFFFFFFF_12D04E98 00000000_12586FF0 00000000_0000030F 00000000_131D70E0 *.....}+q......?0...............\*
_ AR0 00000ED4 00000000 FFFFFFFF FFFFFFFF FFFFFFFF FFFFFFFF FFFFFFFF FFFFFFFF *...M............................*
_ AR8 FFFFFFFF FFFFFFFF FFFFFFFF FFFFFFFF FFFFFFFF FFFFFFFF 00000000 00000000 *................................*
Any Questions?
Notes: <implied click1> Any questions?